## Slide 1: (*) Design (VHDL) (*) Verification (System Verilog)
Presented by:
  Omer Shaked
  Beeri Schreiber
The SPI Project
27.09.2011

## Slide 2: Background - SPI
Asynchronous serial data link standard
Operates in full duplex mode
Devices communicate in master/slave mode
  the master device initiates the data frame.

## Slide 3: Protocol - SPI
The master configure the clock polarity and phase with respect to the data

## Slide 4: Project Goals
Implement SPI Master and SPI Slave
Implement SPI Master and Slave Hosts
Build Test Benches in System Verilog:
  Individual TB for SPI Master and SPI Slave
  Top TB for the entire system

## Slide 5: Implementation Main Problem
SPI Clock’s frequency and Polarity may change during runtime.
Therefore – SPI Clock cannot be placed in the global nets.

## Slide 6: Solution
SPI Master and Slave works with the System Clock.
Master:
SPI Clock is generated from the System Clock, using counter.
Slave:
SPI Clock (spi_clk) is derivate.
SPI Clock Event
(MSB = ‘1’)

## Slide 7: Top Architecture
Slave
Host
Master
Host
Wishbone
Slave
Interface
SPI
Master
Interface
SPI
Slave
Interface
RAM
Interface
RAM

## Slide 8: Master Architecture
SPI
Master
FIFO
Wishbone Slave
Controller
SPI Interface
Wishbone Interface
Master Host
Dec. RAM
Enc. RAM
M.P. Encoder
M.P. Decoder
MUX
‘0’
Checksum
Checksum
Implementation for all components is done!

## Slide 9: Slave Architecture
SPI
Slave
SPI Interface
Message Pack Decoder
Message Pack Encoder
Type
Register
RAM
Controller
Internal
Registers
MUX
RAM Interface
Slave Host
RAM
Not implemented yet
CPOL, CPHA
DEC
FIFO

## Slide 10: Simulations
VHDL TB has been performed on RAM, FIFO, Checksum, Message Packs, SPI Master
System Verilog TB should be written for the following:
  Individual TB for SPI Master and Slave
  Whole System (Including Wishbone Interface)

## Slide 11: Directory Structure
All project files are saved to SVN.

## Slide 12: Schedule
SPI Slave – 24.10.2011
Slave RAM Controller – 24.10.2011
Master Host and Slave Connection – 24.10.2011
Verification schedule is unknown yet.

## Slide 13: Verification Plan (1)
SPI Master:
  Run with all 4 possible options of CPOL and CPHA.
  Validate that clock is divided correct for minimum and maximum register value.
  FIFO empty (should stop SPI Master transaction).
  Register change during active transaction (Should cause error)
  Operation with single / multiple slaves
  During RESET, change inputs. Validate outputs are in their default value.

## Slide 14: Verification Plan (2)
SPI Slave:
  Run with all 4 possible options of CPOL and CPHA.
  Negate SPI_SS in the middle of the transaction.
  SPI_CLK stops for a long time (time out).
  Data from RAM is not valid when it should be.
  Register change during active transaction (Should influence after transaction only)
  During RESET, change inputs. Validate outputs are in their default value.

## Slide 15: Verification Plan (3)
Top Test Bench:
  Run with all 4 possible options of CPOL and CPHA.
  Run with different SPI_CLK frequencies.
  Write data to random address in RAM, then read from it. Validate data match.
  Perform “Write-write-read-write-read”.
  Perform “Write-read-read-write-read”.
  Write Single (burst size of 1), and Burst.
  Write / read to / from non-existing register address.
  Write to valid address, but burst length exceeds from valid address.
  Stop transaction in the middle (Negate WBM_CYC).
  Perform RESET in the middle of the transaction.