## Slide 1
Presented by:
Omer Shaked
Beeri Schreiber
Serial Peripheral Interface
Final Project Presentation
27.12.2011

## Slide 2: Project Requirements
Implement SPI Master and SPI Slave cores (VHDL)
Implement Master and Slave hosts (VHDL)
Verify the entire design (SystemVerilog)

## Slide 3: SPI In General
Serial data link standard
Operates in full duplex mode
Devices communicate in master/slave mode
  Single master, multiple slaves
  The master initiates the data frame

## Slide 4: SPI In General (Cont.)
The interface is consumed of four signals:
  SPI_CLK: Serial Clock (output from master)
  SPI_MOSI: Master Output, Slave Input
  SPI_MISO: Master Input, Slave Output
  SPI_SS: Slave Select (output from master).

## Slide 5: SPI In General (Cont.)
The master configures the clock polarity and phase

## Slide 6: Wishbone In General
Please add general description of WB

## Slide 7: Implementation Stages Unit Level
Design of SPI Master and SPI Slave cores
Design internal blocks of master and slave hosts
SPI Master and SPI Slave individual Test Benches

## Slide 8: Implementation Stages Top Level
Integration of SPI cores
Integration of master and slave hosts
SPI top test bench
Top architecture test bench

## Slide 9: SPI Core Design
Four main interfaces:
SPI Core
SPI Interface
FIFO Interface
CFG interface
Received Data Interface
Generic word length
Generic number of slaves

## Slide 10: Top Architecture Design
Slave
Host
Master
Host
Wishbone
Slave
Interface
SPI
Master
Interface
SPI
Slave
Interface
RAM
Interface
RAM
Master host implements Wishbone slave interface
Hosts communicate via SPI
Slave host implements RAM interface

## Slide 11: Master Host Design
SPI
Master
FIFO
Wishbone Slave
Controller
SPI Interface
Wishbone Interface
Master Host
Dec. RAM
Enc. RAM
M.P. Encoder
M.P. Decoder
MUX
‘0’
Checksum
Checksum

## Slide 12: Slave Host Design
RAM
SPI
Slave
RAM
Controller
RAM Interface
Slave Host
Read MUX
FIFO
Dec. RAM
M.P. Decoder
Checksum
M.P. Encoder
Checksum
Enc. RAM
Slave Host Controller
Registers
SPI Interface

## Slide 13: Verification Plan
Basic block-level VHDL TBs during design stage
SystemVerilog TBs
  SPI Master
  SPI Slave
  SPI Top
  Architecture Top

## Slide 14: Verification Plan (Cont.)
Main verification principles
  Use of randomly generated values
  Coverage collection
  Automatic scoreboarding
  SPI cores – include possible edge cases
  Top architecture – only basic functionality

## Slide 15: SPI Master Test Bench
SPI Master
(DUT)
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Generator
and
Driver
Receiver
3
4
Scoreboard
5
CFG interface
CFG_DUT
6
7
Status | Test Name
 | Normal burst
 | All CPOL, CPHA configurations
 | All SPI clock frequencies
 | Reset
 | Forbidden Configuration
+ | FIFO Error
+ | Illegal SPI Clock Frequencies

## Slide 16: SPI Slave Test Bench
SPI Slave
(DUT)
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Generator
Receiver
3
Scoreboard
6
CFG interface
CFG_DUT
7
8
SPI Master
BFM
4
5
Status | Test Name
 | Normal burst
 | All CPOL, CPHA configurations
 | Max SPI clock frequency
 | Reset
 | Configuration during transmission
 | Timeout
 | Interrupt

## Slide 17: SPI Top Test Bench
SPI Master
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Receiver
Scoreboard
5
CFG interface
CFG_DUT
6
4
SPI Slave0
Generator
and
Driver
DUT
3
7
SPI Slave1
SPI Slave2
SPI Slave3
SPI Interface
FIFOI interface
CFG interface
Status | Test Name
+ | Normal burst
+ | All CPOL, CPHA configurations
+ | Different SPI clock frequencies
+ | Max SPI clock frequency
+ | Generics

## Slide 18: Top Test Bench (UVM 1.1)
Master
Host
Slave
Host
SPI
I/F
External
RAM
WBS
DUT
Driver
Monitor
Sequencer
Agent
Scoreboard
UVM_ENV
UVM_TEST
1
2
3
4
5
Status | Test Name
 | All burst lengths
 | All CPOL, CPHA configurations
 | All SPI clock frequencies
 | Burst length exceeds RAM address
 | Transaction interrupted
 | Reset in middle of transaction

## Slide 19: SV Verification Summary
COVERGROUP COVERAGE: ---------------------------------------------------------------------------------------------------- Covergroup Metric Goal/ Status At Least ---------------------------------------------------------------------------------------------------- TYPE /top/master_host_monitor/cov_trans 100.0% 100 Covered Coverpoint cov_trans::length 100.0% 100 Covered Coverpoint cov_trans::init_addr 100.0% 100 Covered Coverpoint cov_trans::div_factor 100.0% 100 Covered Coverpoint cov_trans::cpol_cpha 100.0% 100 Covered CLASS master_host_monitor TOTAL COVERGROUP COVERAGE: 100.0% COVERGROUP TYPES: 1
Total of 8 bugs were found
  SPI Master – 2
  SPI Slave – 3
  Top – 2
Reached 100 % coverage rate for all TBs

## Slide 20: Summary & Conclusions
A lot more than the original project
Well-organized development methodology
Relatively fast completion of the project
Very enjoyable and fruitful

## Slide 21: The End
Thanks to both of our supervisors !
Comments
&
Questions