## Slide 1
Presented by:
Omer Shaked
Beeri Schreiber
Serial Peripheral Interface
Final Project Presentation
27.12.2011
Supervised by:
Tal Yahav
Leon Polishuk

## Slide 2: Project Requirements
Implement SPI Master and SPI Slave cores (VHDL)
Implement Master and Slave hosts (VHDL)
Verify the entire design (SystemVerilog)

## Slide 3: SPI Protocol Description
Serial data link standard
Operates in full duplex mode
Devices communicate in master/slave mode
  Single master, multiple slaves
  The master initiates the data frame

## Slide 4: SPI Interface Description
The interface is consumed of four signals:
  SPI_CLK: Serial Clock (output from master)
  SPI_MOSI: Master Output, Slave Input
  SPI_MISO: Master Input, Slave Output
  SPI_SS: Slave Select (output from master)

## Slide 5: SPI Clock Configuration
The master configures the clock polarity and phase

## Slide 6: SPI Master Burst Waveform
End of Reset
Enable
SPI Slave
Disable
SPI Slave
SPI_CLK
Divide Factor : 2
SPI_CLK
Divide Factor : 4
FIFO:
Request for data
Data is Valid
a
b
Write to Registers:
Data (0x4) + data_valid
SPI Response:
Register acknowledge
Output data from
SPI Slave is valid
1
2
3
4
5
6
7
8
9

## Slide 7: SPI Slave Burst Waveform
FIFO:
Request for data
Data is Valid
End of Reset
SPI_SS is
De-activated
Data is sampled after
SPI_CLK rising edge
Data is propagated after
SPI_CLK falling edge
4
a
b
SPI_SS is
Activated
2
1
End of Transaction
Dout is valid
3
6
5

## Slide 8: Wishbone Description
Wishbone: Flexible design methodology for use with semiconductor IP cores
Wishbone Interface is used, in this project, to read and write data.

## Slide 9: Wishbone Description: Write Burst
Start of Cycle
Data Acknowledged
Repeat last transaction
New Input Data
Writing
Address
Burst Length
Output Data

## Slide 10: Wishbone Description: End of Write Burst
End of Cycle
New Input Data
Writing
Address
Burst Length
Input Data
Last Strobe
Data with no
strobe (Ignored)

## Slide 11: Wishbone Description: Read Burst
Reading
Address
Burst Length
Output Data
Start of Cycle
Data Valid
Repeat last transaction
Continue to
next transaction
New Output Data

## Slide 12: Wishbone Description: End of Read Burst
End of Cycle
Continue to next transaction
New Output Data
Reading
Address
Burst Length
Output Data
Last Strobe

## Slide 13: Implementation Stages Unit Level
Design of SPI Master and SPI Slave cores
Design internal blocks of master and slave hosts
SPI Master and SPI Slave individual Test Benches

## Slide 14: Implementation Stages Top Level
SPI top test bench (SPI Slave  SPI Master)
Top architecture test bench (Whole system)

## Slide 15: SPI Core Design
Four main interfaces:
SPI Core
SPI Interface
FIFO Interface
Configuration interface
Received Data Interface
Generic word length
Generic number of slaves

## Slide 16: Top Architecture Design
Slave
Host
Master
Host
Wishbone
Slave
Interface
SPI
Master
Interface
SPI
Slave
Interface
RAM
Interface
RAM
Master host implements Wishbone slave interface
Hosts communicate via SPI
Slave host implements RAM interface

## Slide 17: Master Host Design
SPI
Master
FIFO
Wishbone Slave
Controller
SPI Interface
Wishbone Interface
Master Host
Dec. RAM
Enc. RAM
M.P. Encoder
M.P. Decoder
MUX
‘0’
Checksum
Checksum

## Slide 18: Slave Host Design
RAM
SPI
Slave
RAM
Controller
RAM Interface
Slave Host
Read MUX
FIFO
Dec. RAM
M.P. Decoder
Checksum
M.P. Encoder
Checksum
Enc. RAM
Slave Host Controller
Registers
SPI Interface

## Slide 19: Verification Plan
Basic block-level VHDL TBs for SPI cores during design stage
SystemVerilog TBs
  SPI Master
  SPI Slave
  Top: SPI Master + Slave
  Top Architecture (Whole system)
Not part of the original verification plan

## Slide 20: Main Verification Guidelines
  Randomly generated values
  Functional Coverage collection
  Automatic scoreboarding
  SPI cores – includes possible edge cases
  Top architecture – only basic functionality

## Slide 21: SPI Master Test Bench
SPI Master
(DUT)
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Generator
and
Driver
Receiver
3
4
Scoreboard
5
CFG interface
CFG_DUT
6
7
Status | Test Name
Passed | Simple burst
Passed | All CPOL, CPHA configurations
Passed | All SPI clock frequencies
Passed | Reset drives outputs to default values
Passed | Forbidden Configuration
Passed | FIFO Error (Not responding)
Passed | Illegal SPI Clock Frequencies

## Slide 22: SPI Slave Test Bench
SPI Slave
(DUT)
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Generator
Receiver
3
Scoreboard
6
CFG interface
CFG_DUT
7
8
SPI Master
BFM
4
5
Status | Test Name
Passed | Simple burst
Passed | All CPOL, CPHA configurations
Passed | Max SPI clock frequency
Passed | Reset drives outputs to default values
Passed | Configuration during active transmission
Passed | Timeout
Passed | Interrupt

## Slide 23: SPI Top Test Bench
SPI Master
SPI Interface
FIFOI interface
Generator
and
Driver
Receiver
1
2
Receiver
Scoreboard
5
CFG interface
CFG_DUT
6
4
SPI Slave0
Generator
and
Driver
DUT
3
7
SPI Slave1
SPI Slave2
SPI Slave3
SPI Interface
FIFOI interface
CFG interface
Status | Test Name
Passed | Simple burst
Passed | All CPOL, CPHA configurations
Passed | Different SPI clock frequencies
Passed | Max SPI clock frequency
Passed | Generics

## Slide 24: Top Test Bench (UVM 1.1)
Driver
Monitor
Sequencer
Agent
Scoreboard
UVM_ENV
UVM_TEST
Master
Host
Slave
Host
SPI
I/F
External
RAM
WBS
DUT

## Slide 25: Top Test Bench (UVM 1.1)
Status | Test Name
Passed | All burst lengths
Passed | All CPOL, CPHA configurations
Passed | All SPI clock frequencies
Removed. Not relevant. | Burst length exceeds RAM address
Removed. Not relevant. | Transaction interrupted
Removed. | Reset in middle of transaction

## Slide 26: SV Verification Summary
COVERGROUP COVERAGE: ---------------------------------------------------------------------------------------------------- Covergroup Metric Goal/ Status At Least ---------------------------------------------------------------------------------------------------- TYPE /top/master_host_monitor/cov_trans 100.0% 100 Covered Coverpoint cov_trans::length 100.0% 100 Covered Coverpoint cov_trans::init_addr 100.0% 100 Covered Coverpoint cov_trans::div_factor 100.0% 100 Covered Coverpoint cov_trans::cpol_cpha 100.0% 100 Covered CLASS master_host_monitor TOTAL COVERGROUP COVERAGE: 100.0% COVERGROUP TYPES: 1
Total of 7 major bugs were found and fixed:
  SPI Master – 2
  SPI Slave – 3
  Top – 2
Reached 100 % functional coverage for all TBs

## Slide 27: Summary & Conclusions
A lot more than the original project
  Design:
  Master and Slave host implementation, instead of only SPI Master and Slave
  Verification:
  Implemented 4 TBs instead of 3 TBs
  All major SystemVerilog features have been used
  Usage of UVM 1.1

## Slide 28: Summary & Conclusions
A lot more than the original project
Well-organized development methodology
Relatively fast completion of the project
Very enjoyable and fruitful

## Slide 29: The End
Thanks to both of our supervisors !
Comments
&
Questions